| When to Use This Form | This Packet is to be used in conjunction with procedure P-192.501. |
| --- | --- |
| Reviewed Procedures | P-192.501 Steel Pipeline Pressure Test Requirements |
|  | The applicable sections of the above procedure(s) shall be reviewed prior to completing this form. |
| Documentation Procedure | Copy form and replace original. Do not mark up the original copy of this form. Complete all sections of the form. If the pipeline is exposed for any reason (external or internal) complete Form WTG 1100. Document any repairs required due to rupture or leak using packet F-192.305. Attach pressure recording charts, test instrument calibration data. For unsuccessful tests complete Unsuccessful Hydrostatic Test section of this form. Have test supervisor sign form. Send a copy of the form to engineer to establish MAOP of the pipeline. See Form F-192.619. Place in DOT file. Keep most current test. Retain Records for the Life of the Pipeline System. |

Description

| Name of Individual Responsible for Testing: |
| --- |
| Operator: |
| System or Facility Tested: | Start Date: | Start Time: |
|  | Stop Date: | Stop Time: |
| Extent of Test: From Station: | To Station: |
| Test Medium: Water Other: | Inhibitor: Yes No |
| Test Company: | Inhibitor Type: | Inhibitor Rate: |
| Purpose: Initial Construction Pretest Retest Repair or replacement |
| Source of Water Fill: |
| Leak Detection Material Type: | Rate: |
| Pressure Pump Location: | Sta: | MP: | Elev.: |
| Certified Gauge Location: | Sta: | MP: | Elev.: |
| Certified Gauge Calibration Date: | Serial Number: |
| Pressure Recorder Serial Number: |
| Pipe Temp. Recorder Serial Number: |
| Elevation and Calculated Pressure and Critical Points During Test Period: |
| High Point: | Elev: | Press. Min: | Press. Max: |
| Low Point: | Elev: | Press. Min: | Press. Max: |
| Certified Gauge: | Elev: | Press. Min: | Press. Max: |

Pipe Data

| From Sta. No. to Sta. No. | OD (inches) | Wall (inches) | Grade | SMYS | Seam FAC “E” | Design FAC “F” | Internal Design Press. |
| --- | --- | --- | --- | --- | --- | --- | --- |

Component Data

| Description | Manufacturer | SMYS | MAOP/MOP |
| --- | --- | --- | --- |
| Weakest Component other than Pipe: |
| MAOP/MOP of Weakest Component: |

Pressure and Temperature Data

| No | Time | Gauge Press | Chart Press | Pipe Temp | Ambient | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |
| 11 |  |  |  |  |  |  |
| 12 |  |  |  |  |  |  |
| 13 |  |  |  |  |  |  |
| 14 |  |  |  |  |  |  |
| 15 |  |  |  |  |  |  |
| 16 |  |  |  |  |  |  |
| 17 |  |  |  |  |  |  |
| 18 |  |  |  |  |  |  |
| 19 |  |  |  |  |  |  |
| 20 |  |  |  |  |  |  |
| 21 |  |  |  |  |  |  |
| 22 |  |  |  |  |  |  |
| 23 |  |  |  |  |  |  |
| 24 |  |  |  |  |  |  |
| 25 |  |  |  |  |  |  |
| 26 |  |  |  |  |  |  |
| 27 |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |
| 30 |  |  |  |  |  |  |

Summary of Test

| Test Medium: | Min. Test Pressure: |
| --- | --- |
| Test Duration: | Test pressure (Corrected for high elevation): |
| Piping was buried during test | Piping was exposed & inspected during test |
| Test Supervised by: |
| Certified by Division or Project Engineer: |
| Approved by Division or Project Manager: |
| Documents Attached: Pressure Chart Temp. Chart Sketch or Diagram Profile (required if elevation change is > 100') |

Unsuccessful Hydrostatic Test

| Pipeline/Line Section: |
| --- |
| Pipe Data: | O.D.: | W.T.: | Grade: | Year Built: |
| Seam Type: SMLS ERW SAW Spiral Flash Weld Lap Weld |
| Internal Pressure at 100% SYMS: |
| Joint Type: Acetylene Arc Weld Mechanical |
| Pipe Manufacturer: |
| Design Test Pressure Max: | Min: |
| Test Section Number: | From Sta.: | (MP: ) | To Sta.: | (MP: ) |
| Reason for Unsuccessful test: Leak Rupture |
| Metallurgical Report Review: Yes No |

| Leak Data |
| --- |
| Was leak found? |
| Yes | Date: | Time: | Station: | Elevation: |
|  | Time on Test when leak was found: |
|  | Leakage Rate: |
|  | Pressure at leak when discovered: |
|  | Location: Body Seam |
| No |
| Description and possible causes of leak: |
| Rupture Data |
| Location: | Station: | Elevation: |
| Date of rupture: | Time of Rupture |
| Pressure at rupture: | Time on Test before rupture: |
| Location: Body Seam |
| Description and possible causes of rupture: |